## Slide 1: Electrical Power Storage 96% Round-Trip Efficiency
LightFuel® Array
1 MW1.6 MW hydrogen hhv
on diurnal basis
Hydrogen Storage
Fuel Cell
60% eff.
Power
Interface
Unit
SMPS
H2
96% R-T electrical efficiency in sunlight cost to store$0.08/kWh
On-demand
0.96 MW OUT time-shifted
Excess Solar,
1.0 MW IN
Wind, Off-peak grid
H2O
2020-2-02 LightFuel Solar-Amplified Electrolysis Copyright 2020 LightFuel Co.
Notes: LightFuel’s efficient diurnal hydrogen production results in 84% Round-Trip (R-T) efficiency when coupled with a fuel cell operating at 60% efficiency, and on a diurnal 100% capacity basis. Even higher R-T efficiency of at least 96% is obtained windowing and variable voltage. For comparison, a 70% efficient alkaline electrolyzer and 60% fuel cell has a round-trip efficiency of only 42%. Today’s batteries can achieve 96% but only with low-draw and for short times. Let’s step through the process…..

## Slide 2: Electrical Power Storage System diagram: Direct-use
LightFuel® Array
Hydrogen Storage
Fuel Cell
Power
Interface
Unit
Switched Mode
P. S.
1 MW OUT to load
Direct-use Solar,
1 MW ENERGY IN
Wind, Off-peak grid
WITH load: solar or wind power is used directly.
2020-2-02 LightFuel Solar-Amplified Electrolysis Copyright 2020 LightFuel Co.
Notes: When load is present: solar, wind, and other intermittent sources, renewable or non, are used directly.
Conversions:
MMSCF (15-21C) = 26,279 NM^3 (0C) both at 1 ATM
NM^3 = 1,000 l = 0.09 kg H2
1 kg H2 = 11.13 NM^3 = 11,126 l
1 ATM ~ 1 bar = 14.7 psi = 0.1 Mpa
1 U.S. ton = 907.2 kgs
H2 HHV/LHV = 39.4kWh/33.3kWh/kg H2
= 3.54 kWh/NM^3/2.99 kWh/NM^3
= 325btu/275btu/FT^3 H2
HHV includes latent heat of vaporization if captured

## Slide 3: Electrical Power Storage System diagram: Storage
LightFuel® Array
1 MW1.6 MW
hydrogen hhv
Hydrogen Storage
Fuel Cell
Power
Interface
Unit
SMPS
H2
Excess Solar,
1 MW ENERGY IN
Wind, Off-peak grid
NO LOAD: Excess power produces hydrogen, STORED.
2020-2-02 LightFuel Solar-Amplified Electrolysis Copyright 2020 LightFuel Co.
Notes: Excess renewable and/or off-peak grid power is converted into hydrogen with sunlight and the LightFuel Solar-Assisted Electrolyzer. For each MWh of electrical power in, LightFuel Solar-Assisted Electrolyzer produces hydrogen with HHV energy equivalent of 1.6Mh at optimized operating hours, and even more.

## Slide 4: Electrical Power Storage System diagram: Demand
LightFuel® Array
Hydrogen Storage
Fuel Cell
Power
Interface
Unit
SMPS
H2
Excess Solar,
1 MW ENERGY IN
Wind, Off-peak grid
PIU calls for power: Stored hydrogen flows to Fuel Cell
2020-2-02 LightFuel Solar-Amplified Electrolysis Copyright 2020 LightFuel Co.
Notes: When the Power Interface Unit calls for power, stored hydrogen, as well as oxygen, are delivered to the fuel cell. The oxygen can increase the efficiency of the fuel cell to 60% or more.

## Slide 5: 1 MW Storage System diagram: Delivery
LightFuel® Array 1 MW
0.56 Hectare
Hydrogen Storage
Fuel Cell
60% eff.
Power
Interface
Unit
SMPS
H2
96% R-T electrical efficiency in sunlight $0.03/kWh storage cost
On-demand
0.96 MW OUT time-shifted
Excess Solar,
1.0 MW IN
Wind, Off-peak grid
H2O
2020-2-02 LightFuel Solar-Amplified Electrolysis Copyright 2020 LightFuel Co.
Notes: And the fuel cell delivers power to the grid.
Capital cost is projected to be $1,818 kW-1 Cost to store a kWh is $0.03 USD. Basis: 10 year project life, optimized operating hours, 24MWh/day, 4,430 LF panels at 5,625 m2 installation, and projected pilot installed cost of $500 USD / panel for $2.2M USD installation.
The high 96% Round-Trip R-T efficiency can actually increase to >100% because our LightFuel electrolyzer has a second power input that is sunlight. So on an electrical energy basis (EEB) our electrical efficiency can peak at 140% during peak hydrogen production. We’re not breaking the first law of thermodynamics: energy is conserved.
In comparison, for an alkaline electrolyzer at 70% efficiency, the round-trip storage efficiency, using the same 60% efficient fuel cell, is 42%. So, in comparison, LightFuel storage can return >2X kWh back to the grid.

## Slide 6: 1 MW Storage Project Proposed
1 MW Capacity
0.56 Hectare (1.4 acres)
$1,818 kW-1
625 KGs/day Hydrogen
or
1 MW / Hour stored @ $0.03/kWh
On-demand
0.96 MW ENERGY OUT time-shifted
Excess Solar,
1 MW ENERGY IN
Wind, Off-peak grid
1 MW/Hour Storage OR
625 KGs/Day Hydrogen
0.56 Hectare (1.4 acres) Installation
2020-2-02 LightFuel Solar-Amplified Electrolysis Copyright 2020 LightFuel Co.
Notes: In summary, a 1 MW capacity (i.e. 24 MWh/Day consumption at 100% operating capacity) LightFuel plant will produce 625 kgs of hydrogen per day for mobility -- Fuel Cell Electric Vehicles, including FCEV trains, buses, trucks, and cars. Or, for storing 1 MW/hour of electrical energy, The LightFuel Array would occupy an area of 0.56 hectare (1.4 acres).